EPIC Partner Class -- 2013
Soldering
and
Arduinos

---
Soldering
- Soldering is the joining of
  metal objects together.
  A filler metal (“solder”) is
  melted and flowed into the joint.
- Soldering was practiced in
  ancient Egypt at least
  5000 years ago
- Soldering is used to attach
  electronic components to
  a board, and also for jewelery
  and other applications

---
Soldering Safety
- The iron gets hot!
  Don't burn yourself. Careful not to splash solder
- Solder is made of lead, which is poisonous
  Wash your hands when you are done; don't eat or drink while soldering
- Snipped component leads fly at high speeds
  Close your eyes or cover with your hands

---
What's an Arduino?
A: A tiny computer
The black thing with all the legs
is a tiny computer called
a microcontroller
They can be programmed
in C or C++
They are used in lots of
things around your house
(microwave, stereo, TV...)

---
Micro-what?
- Q:	What exactly is a microcontroller (uC)?
  A:	Just a very small (usually single-chip) computer
- Q:	What features must a microcontroller have?
  A:	A central processing unit (CPU)
  Program memory (usually flash)
  Data memory (at least registers, usually RAM too)
  Some input / output
- Q:	What other features may a uC have?
  A:	Counter/timer units, serial ports,
  A/D and D/A converters, plus sometimes special
  features such as USB, WiFi, light dimmers....

---
Essential uC Components
Program Memory
Instructions (code)
Registers
(temporary storage)
Central
Processing
Unit
Input/
Output
External
Devices
Data Memory
(variables)

---
Arduino “Sketch” Example
It's almost exactly “C”, but...
No “#includes” unless you use
a special library
Special function setup()
called once when program starts
pinMode() tells the Arduino
whether a pin is for input
our output
Special function loop()
called forever after setup()
DigitalWrite() sets a pin to
a specific “logic level”:
HIGH = 5V
LOW = 0V
No “printf” since there is no
keyboard / screen attached!
Special function delay()
stops the program for specified
number of milli-seconds
(1/1000 second steps)

---
Circuit Example
Power supply
(two AA batteries)
Micro-
controller
LED
(output device)
push-button
(input device)
resistor to limit
LED current

---
More about Input and Output
- Two types of devices:
  - Digital
    - On / Off only (like an LED or push-button)
    - Sometimes used in groups (i.e. for a keypad)
    - Can form a bus (special group with data and control)
      for example to control an LCD display
  - Analog
    - Variable level/speed (like a knob or a motor)
    - For input, use an ADC (analog-to-digital converter)
    - For output, use a DAC (digital-to-analog converter)
    - Often used for things like ultrasonic range finders,
      light sensors or speed control of motors

---
Programming considerations
- Just like programming a “real computer”, except:
  - Generally C/C++ is the only language choice
  - Program memory is small! Programs must be short
  - Data memory is small! Only a few variables
  - Often there is no keyboard or display, so functions like printf() are not useful
  - Floating point math is “expensive” so best use only integers
  - For efficiency, pick variables of the right size
    (use a char if 8 bits is enough)